## Slide 1
PWS
Switch
120/240 VAC
Relay
12V Coil
40A, SPDT
12 VDC
Battery
6A
30A
1A
6A
SPARE
SPARE
12V Fuse Block
P2 – to 12V/5V Converter
Heater Relay
Coil on P3
200W
Heater
100W
Heater
P3 – to Control Board
Circulation Fan
6 AWG
6 AWG
18 AWG
10 AWG
24 AWG
18 AWG
10 AWG
6 AWG
6 AWG
Designer: Noah Daugherty | Date: 4/12/2020
12V Power Distribution
GT4823 – Infant Incubator

## Slide 2
5A
1A
6A
SPARE
SPARE
SPARE
5V Fuse Block
+
+
-
-
P1 – to Fuse 1
12V -> 5V
Buck Converter
+
-
Raspberry Pi
+
-
Monitor
P3 – To Control Board
14 AWG
Designer: Noah Daugherty | Date: 4/12/2020
5V Power Distribution
GT4823 – Infant Incubator
20 AWG
22 AWG
20 AWG
14 AWG

## Slide 3
P1 – to Fuse 4
P2 – to Fuse 3
Raspberry Pi GPIO Connection
Temperature Control Panel
Ambient Temperature Sensors
Neonate Temperature Sensor
Weight/Apnea Sensors
SPO2 Sensor
Temperature and Humidity Sensor
Input Fan Control
Control Board
Heater Relay
Contact on P1
Designer: Noah Daugherty | Date: 4/12/2020
Control Board I/O
GT4823 – Infant Incubator

## Slide 4
Designer: Noah Daugherty | Date: 4/12/2020
Sensor Connector Layout
GT4823 – Infant Incubator
Incubator Side View
Head
Foot
J1
J2
J3
J4
J5
J6
J# | Type | Connection
J1 | M8 3-wire | Monitor
J2 | M8 3-wire | Temp/Humidity Sensor
J3 | M8 4-wire | Neonatal Temp Sensor
J4 | M12 ???-wire | Weight/Apnea Sensor
J5 | ??? | SpO2 Sensor
J6 | M12 5-wire | Ambient Temp Sensors

## Slide 5
Designer: Noah Daugherty | Date: 4/12/2020
Temperature Control Interface
GT4823 – Infant Incubator
31
34
35
32
33
36
37
SETPOINT
TEMP OK
ALARM OFF
I
O
LIGHTING
5cm x 10 cm